## Slide 1: Geometric Event Finding Programming Lesson
March 2006
Notes: 1

## Slide 2: Geometric Event Finding: Overview
Problem statement:
  Write a program that determines when a point target is visible, as seen from a surface point on an extended body.
    Assume that a second extended body may occult the target.
    Account for the possibility that the body on which the surface point is located may occult the target.
  Concrete application:
    Within the time interval
      2004 May 2 TDB
      2004 May 6 TDB
    determine when the Mars Express orbiter is visible from the DSN station DSS-14.
    Account for possible occultation by the earth or by Mars.
    Produce a SPICE window representing the visibility period.
Notes: 2

## Slide 3: Visibility Geometry
Elevation
angles
Basis vectors of
topocentric frame
Mars
Earth
MEX:
Occulted
MEX:
Visible
Elevation
Limit
DSS-14
MEX: not occulted, but
below elevation limit.
Not visible.
Notes: 3